## Slide 1: Design and Implementation of a 64-bit RISC-V IMAC Architecture with Privilege Modes and Level-1 Caches
Final Presentation

## Slide 2: Presenters
Name | ID
Ahmed Hamdi Ibrahim | 19015219
Basmala El-Dabaa Fayez | 19015517
Ziad Taha Mohamed Taha | 19015723
Mohamed Maged Abdulhalim | 19016475
Mohamed Morsi Abd-Elsamee | 19016505
Mohamed Mohamed Tariq | 19017130
Ali Khaled Mohamed | 19017540
Aly Mohamed El-Ruby | 19016023
Nsreen Nashaat Abdo | 18011992
Hythem Ahmed Shaban | 19016856

## Slide 3
Introduction
Design
  Base I ISA
  C-extension
  M-extension
  A-extension
  Caches
  Branch Prediction
  Privileged ISA
Verification
FPGA
ASIC
Outline

## Slide 4: Chapter 1 Introduction

## Slide 5: Introduction
Motivation:
- Chose a 64-bit RISC-V IMAC core with privilege modes and level 1 caches to run OS such as LINUX and assembly programs.
- It aims to expand into automotive, aerospace, and telecommunications markets, standardize extensions, and improve compatibility.
- Being open-source provides programmers maximum hardware access and software flexibility.
- A 64-bit architecture supports modern software applications, operating systems,
and databases, with enhanced security features like larger cryptographic keys.

## Slide 6: Introduction
History:
1. Developed at UC Berkeley's Parallel Computing Lab
from 2010.
2. Open-source instruction set architecture (ISA) known for
simplicity and modularity.
3. Widely adopted across diverse applications from IoT to
high-performance computing for its customizable and
scalable design.

## Slide 7: Introduction
What is RISC-V
1.Open Source
2.Simplicity and Flexibility
3.Modular Design
4.Scalability
5.Community-Driven
6.Adoption

## Slide 8: Introduction
Objectives:
1. Design a RISC-V Core Processor.
2. Incorporate Cached Memory.
3. Support for Privileged Modes.
4. Verification and Testing.
5. Documentation and Analysis.

## Slide 9: Introduction
RISV-V Extensions:

## Slide 10: Introduction
PRIVILEGED MODES:
M – Machine
U – User
S – Supervisor

## Slide 11: Introduction
NON-PRIVILEGED ISA EXTENSIONS:
1)I: Extension for general-purpose computing.
2)M: Extension for integer multiplication and division.
3)A: Extension for atomic instructions.
4)C: Extension for compressed instructions.

## Slide 12: Introduction
Why do we need a privileged architecture?
1-We need to manage shared resources
-Memory
-I/O devices
-Cores
2-we need to protect shared resources
3-we need to insulate implementation details
4-to run OS on RISC-V core

## Slide 13: Introduction
Comparison between RISC-V ,ARM and x86
RISC-V: Open source, Use reduced instruction set so
the decoders are simpler.
ARM and x86:widely used, they come with licensing
fees and restrictions, Use complex instruction set so
the decoders are more complex.

## Slide 14: Chapter 2 Implementation of Base-I ISA

## Slide 15: Base-I | RV64I ISA
R-Type
  add(w), sub(w), xor, or, and, sll(w), srl(w), sra(w), slt, sltu
I-Type
  addi(w), xori, ori, andi, slli(w), srli(w), srai(w), slti, sltiu
  lb(u), lh(u), lw(u), ld
  jalr
S-Type
  sb, sh, sw, sd
B-Type
  beq, bne, blt(u), bge(u)
J-Type
  jal
U-Type
  lui, auipc

## Slide 16: Base-I | RV64I Microarchitecture
Subset of Base-I from Harris & Harris Book

## Slide 17: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Add Control Unit
  Pipeline the Single Cycle
  Add Hazard Unit

## Slide 18: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Datapath: start with lw instruction
  Example: lw rd, imm(rs1)
I-Type |  |  |  | 
31:20 | 19:15 | 14:12 | 11:7 | 6:0
imm | rs1 | funct3 | rd | Op
12 bits | 5 bits | 3 bits | 5 bits | 7 bits

## Slide 19: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Datapath: start with lw instruction
  Example: lw rd, imm(rs1)
lw fetch

## Slide 20: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Datapath: start with lw instruction
  Example: lw rd, imm(rs1)
lw Reg Read

## Slide 21: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Datapath: start with lw instruction
  Example: lw rd, imm(rs1)
lw Immediate

## Slide 22: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Datapath: start with lw instruction
  Example: lw rd, imm(rs1)
lw Mem Read

## Slide 23: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath
  Datapath: start with lw instruction
  Example: lw rd, imm(rs1)
PC Increment

## Slide 24: Base-I | RV64I Microarchitecture
Design Methodology:
  Start by designing Single Cycle Datapath

## Slide 25: Base-I | RV64I Microarchitecture
Design Methodology:
  Add Control Unit
op | Instruct | RegWrite | ImmSrc | ALUSrc | MemWrite | ResultSrc | Branch | ALUOp | PCUpdate | ALUControl | 
3 | lw | 1 | 00 | 1 | 0 | 10 | 0 | 00 | 0 | 000 | 
35 | sw | 0 | 01 | 1 | 1 | XX | 0 | 00 | 0 | 000 | 
51 | R-type | 1 | XX | 0 | 0 | 01 | 0 | 10 | 0 | and | 010
 |  |  |  |  |  |  |  |  |  | or | 011
 |  |  |  |  |  |  |  |  |  | add | 000
 |  |  |  |  |  |  |  |  |  | sub | 001
 |  |  |  |  |  |  |  |  |  | slt | 101
99 | beq | 0 | 10 | 0 | 0 | XX | 1 | 01 | 0 | 001 | 
19 | addi | 1 | 00 | 1 | 0 | 01 | 0 | 10 | 0 | 000 | 
111 | jal | 1 | 11 | X | 0 | 00 | 0 | XX | 1 | XXX | 

## Slide 26: Base-I | RV64I Microarchitecture
Design Methodology:
  Add Control Unit

## Slide 27: Base-I | RV64I Microarchitecture
Design Methodology:
  Add Control Unit

## Slide 28: Base-I | RV64I Microarchitecture
Design Methodology:
  Pipeline the Single Cycle
    Add pipelines.

## Slide 29: Base-I | RV64I Microarchitecture
Design Methodology:
  Pipeline the Single Cycle
    Correct Pipelined Datapath. (Rd must arrive at same time as Result)

## Slide 30: Base-I | RV64I Microarchitecture
Design Methodology:
  Pipeline the Single Cycle
    Add Control Unit. (control signals travel with their instructions)

## Slide 31: Base-I | RV64I Microarchitecture
Design Methodology:
  Add Hazard Unit

## Slide 32: Base-I | RV64I Microarchitecture
Subset of Base-I from Harris & Harris Book
Missed Instructions?!

## Slide 33: Base-I | RV64I Microarchitecture
Subset of Base-I from Harris & Harris Book
Instruction | Format | Opcode | Funct3 | Funct7 | Description
lb | I | 0000011 | 0x0 |  | rd = M[rs1+imm][7:0]
lh | I | 0000011 | 0x1 |  | rd = M[rs1+imm][15:0]
lbu | I | 0000011 | 0x4 |  | rd = M[rs1+imm][7:0]
lhu | I | 0000011 | 0x5 |  | rd = M[rs1+imm][15:0]
sb | S | 0100011 | 0x0 |  | M[rs1+imm][7:0] = rs2[7:0]
sh | S | 0100011 | 0x1 |  | M[rs1+imm][15:0] = rs2[15:0]
bne | B | 1100011 | 0x1 |  | if(rs1 != rs2) PC += imm
blt | B | 1100011 | 0x4 |  | if(rs1 < rs2) PC += imm
bge | B | 1100011 | 0x5 |  | if(rs1 >= rs2) PC += imm
bltu | B | 1100011 | 0x6 |  | if(rs1 < rs2) PC += imm
bgeu | B | 1100011 | 0x7 |  | if(rs1 >= rs2) PC += imm
jalr | I | 1100111 | 0x0 |  | rd = PC+4; PC = rs1 + imm
lui | U | 0110111 |  |  | rd = imm << 12
auipc | U | 0010111 |  |  | rd = PC + (imm << 12)

## Slide 34: Base-I | RV64I Microarchitecture
JALR
rd = PC + 4
PC += imm

## Slide 35: Base-I | RV64I Microarchitecture
LUI
rd = imm << 12

## Slide 36: Base-I | RV64I Microarchitecture
AUIPC
rd = PC + (imm << 12)

## Slide 37: Base-I | RV64I Microarchitecture
Instruction | Format | Opcode | Funct3 | Funct7 | Description
lb | I | 0000011 | 0x0 |  | rd = M[rs1+imm][7:0]
lh | I | 0000011 | 0x1 |  | rd = M[rs1+imm][15:0]
lbu | I | 0000011 | 0x4 |  | rd = M[rs1+imm][7:0]
lhu | I | 0000011 | 0x5 |  | rd = M[rs1+imm][15:0]
sb | S | 0100011 | 0x0 |  | M[rs1+imm][7:0] = rs2[7:0]
sh | S | 0100011 | 0x1 |  | M[rs1+imm][15:0] = rs2[15:0]
bne | B | 1100011 | 0x1 |  | if(rs1 != rs2) PC += imm
blt | B | 1100011 | 0x4 |  | if(rs1 < rs2) PC += imm
bge | B | 1100011 | 0x5 |  | if(rs1 >= rs2) PC += imm
bltu | B | 1100011 | 0x6 |  | if(rs1 < rs2) PC += imm
bgeu | B | 1100011 | 0x7 |  | if(rs1 >= rs2) PC += imm
jalr | I | 1100111 | 0x0 |  | rd = PC+4; PC = rs1 + imm
lui | U | 0110111 |  |  | rd = imm << 12
auipc | U | 0010111 |  |  | rd = PC + (imm << 12)

## Slide 38: Base-I | RV64I Microarchitecture
lb(u), lh(u), sb, sh
Handled in Data memory & Load extend

## Slide 39: Base-I | RV64I Microarchitecture
B-Type
Handled in Branch unit

## Slide 40: Base-I | RV64I Design: Fetch Stage

## Slide 41: Base-I | RV64I Design: Fetch Stage
Instruction Memory
  will be discussed in caches

## Slide 42: Base-I | RV64I Design: Fetch Stage
64-bit adder
  It is used to increment PC
I/O | Width | Description
i_64bit_adder_srcA | 64 | Operand 1 (current PC)
i_64bit_adder_srcB | 64 | Operand 2 (64’h4)
o_64bit_adder_result | 64 | Adder result (PC+4)

## Slide 43: Base-I | RV64I Design: Decode Stage

## Slide 44: Base-I | RV64I Design: Decode Stage
Main Decoder
i_opcode
i_funct3
i_funct7
o_imsrc
o_UCtrl
o_resultsrc
o_regwrite
o_memwrite
o_alusrcB
o_branch
o_jump
o_bjreg
o_size
o_LdExt
o_isword
o_imsel
o_aluop
o_new_mux_sel
o_read
riscv_core_main_decoder

## Slide 45: Base-I | RV64I Design: Decode Stage
ALU Decoder
i_funct7_5
i_funct3
i_aluop
o_alu_control
i_funct7_0
i_opcode_5
riscv_core_alu_decoder
Port Name | Direction | Width | Description
i_funct3 | Input | 3 | funct3 bits of the instruction
i_aluop | Input | 1 | Enables the ALU decoder
i_funct7_5 | Input | 1 | Bit number 5 of funct7 part of the instruction
i_funct7_0 | Input | 1 | Bit number 0 of funct7 part of the instruction
i_opcode_5 | Input | 1 | Bit number 5 of opcode part of the instruction
o_alu_control | Output | 4 | Specifies the ALU operation

## Slide 46: Base-I | RV64I Design: Decode Stage
Main Decoder and ALU Decoder
Link

## Slide 47: Base-I | RV64I Design: Decode Stage
Immediate Extend
I/O | Width | Description
i_immextend_imm | 25 | Instr[31:20]
 |  | Instr[31:25], Instr[11:7]
 |  | Instr[31:12]
i_immextend_immsrc | 3 | Type of extend according to instruction type
O_immextend_out | 64 | Extended output

## Slide 48: Base-I | RV64I Design: Decode Stage
Immediate Extend
Format | i_immextend_immsrc | o_immextend_out
I | 3’b000 | {{52{instr[31]}},instr[31:20]}
S | 3’b001 | {{52{Instr[31]}}, Instr[31:25], Instr[11:7]}
B | 3’b010 | {{52{Instr[31]}}, Instr[7], Instr[30:25], Instr[11:8], 1’b0}
J | 3’b011 | {{44{Instr[31]}}, Instr[19:12], Instr[20], Instr[30:21], 1’b0}
R | 3’b100 | {32{instr[31]} ,instr[31:12], {12{1'b0}}}

## Slide 49: Base-I | RV64I Design: Execute Stage

## Slide 50: Base-I | RV64I Design: Execute Stage
ALU
I/O | Width | Description
i_alu_srcA | 64 | Operand 1
i_alu_srcB | 64 | Operand 2
i_alu_control | 4 | ALU operation
i_alu_isword | 1 | Specifies whether the instr is word or not
o_alu_result | 64 | ALU result

## Slide 51: Base-I | RV64I Design: Execute Stage
ALU
i_alu_isword | i_alu_control | Operation
1’b0 | 4’b0000 | o_alu_result = i_alu_srcA + i_alu_srcB
1’b0 | 4’b0001 | o_alu_result = i_alu_srcA - i_alu_srcB
1’b0 | 4’b0110 | o_alu_result = i_alu_srcA ^ i_alu_srcB
1’b0 | 4’b0011 | o_alu_result = i_alu_srcA ¦ i_alu_srcB
1’b0 | 4’b0010 | o_alu_result = i_alu_srcA & i_alu_srcB
1’b0 | 4’b0100 | o_alu_result = i_alu_srcA << i_alu_srcB[5:0]
1’b0 | 4’b0111 | o_alu_result = i_alu_srcA >> i_alu_srcB[5:0]
1’b0 | 4’b1111 | o_alu_result = i_alu_srcA >>> i_alu_srcB[5:0]
1’b0 | 4’b0101 | o_alu_result = i_alu_srcA < i_alu_srcB
1’b0 | 4’b1000 | o_alu_result = i_alu_srcA(U) < i_alu_srcB(U)
1’b1 | 4’b0000 | o_alu_result = i_alu_srcA[31:0] + i_alu_srcB[31:0] (sign ext)
1’b1 | 4’b0001 | o_alu_result = i_alu_srcA[31:0] - i_alu_srcB[31:0] (sign ext)
1’b1 | 4’b0100 | o_alu_result = i_alu_srcA[31:0] << i_alu_srcB[4:0] (sign ext)
1’b1 | 4’b0111 | o_alu_result = i_alu_srcA[31:0] >> i_alu_srcB[4:0] (sign ext)
1’b1 | 4’b1111 | o_alu_result = i_alu_srcA[31:0] >>> i_alu_srcB[4:0] (sign ext)

## Slide 52: Base-I | RV64I Design: Execute Stage
Branch Unit
I/O | Width | Description
i_branch_unit_srcA | 64 | Operand 1
i_branch_unit_srcB | 64 | Operand 2
i_branch_unit_funct3 | 3 | Specifies branch instr
o_branch_unit_istaken | 1 | Flag raised if the condition is true

## Slide 53: Base-I | RV64I Design: Execute Stage
Branch Unit
i_branch_unit_funct3 | Instr. | Operation
3’b000 | BEQ | istaken = i_branch_unit_srcA == i_branch_unit_srcB
3’b001 | BNE | istaken = i_branch_unit_srcA != i_branch_unit_srcB
3’b100 | BLT | istaken = i_branch_unit_srcA < i_branch_unit_srcB
3’b101 | BGE | istaken = i_branch_unit_srcA >= i_branch_unit_srcB
3’b110 | BLTU | istaken = i_branch_unit_srcA(U) < i_branch_unit_srcB(U)
3’b111 | BGEU | Istaken = i_branch_unit_srcA(U) >= i_branch_unit_srcB(U)

## Slide 54: Base-I | RV64I Design: Memory Stage

## Slide 55: Base-I | RV64I Design: Memory Stage
Data Memory
  will be discussed in caches

## Slide 56: Base-I | RV64I Design: Memory Stage
Load Extend
riscv_core_ldextend
i_su_extend
i_r_w_size
i_rdata
o_rdata
Port Name | Direction | Width | Description
i_su_extend | Input | 1 | Determines whether the instruction is signed or unsigned.
i_r_w_size | Input | 2 | Determines the size of the load instruction e.g., LD, LW, LH, LB.
i_rdata | Input | 64 | Data loaded from memory without extend.
o_rdata | Output | 64 | Data loaded from memory after sign/zero extend.

## Slide 57: Base-I | RV64I Design: Writeback Stage

## Slide 58: Base-I | RV64I Design: Writeback Stage
resultsrc | Operation
2’b00 | Writes back the data computed from EX stage
2’b01 | Writes back the data loaded from data memory
2’b10 | Writes back PC+4 for JAL & JALR instructions
Writeback Mux

## Slide 59: Base-I | RV64I Design: Hazard Unit

## Slide 60: Base-I | RV64I Design: Hazard Unit
HU Block Diagram

## Slide 61: Base-I | RV64I Design: Hazard Unit
I/O | Width | Description
i_hazard_unit_rs1_id | 5 | RV64I Hazard Detection Control Signals
i_hazard_unit_rs2_id | 5 | 
i_hazard_unit_rs1_ex | 5 | 
i_hazard_unit_rs2_ex | 5 | 
i_hazard_unit_rd_ex | 5 | 
i_hazard_unit_rd_mem | 5 | 
i_hazard_unit_rd_wb | 5 | 
i_hazard_unit_regwrite_mem | 1 | 
i_hazard_unit_regwrite_wb | 1 | 
i_hazard_unit_resultsrc_ex | 2 | 
i_hazard_unit_pcsrc_ex | 1 | 
I/O | Width | Description
i_hazard_unit_mdone | 1 | RV64M Hazard Detection Signals
i_hazard_unit_mbusy | 1 | 
i_hazard_unit_dcache_stall | 1 | I&D Caches Hazrad Detection Signals
i_hazard_unit_icache_stall | 1 | 
i_hazard_unit_csr_flush_id | 1 | CSR Hazard Detection Signals
i_hazard_unit_csr_flush_ex | 1 | 
i_hazard_unit_csr_flush_mem | 1 | 
i_hazard_unit_csr_flush_wb | 1 | 

## Slide 62: Base-I | RV64I Design: Hazard Unit
I/O | Width | Description
o_hazard_unit_forwarda_ex | 2 | Forwarding Control Signals
o_hazard_unit_forwardb_ex | 2 | 
o_hazard_unit_stall_if | 1 | Stall Control Signals
o_hazard_unit_stall_id | 1 | 
o_hazard_unit_stall_ex | 1 | 
o_hazard_unit_stall_mem | 1 | 
o_hazard_unit_stall_wb | 1 | 
o_hazard_unit_flush_id | 1 | Flush Control Signals
o_hazard_unit_flush_ex | 1 | 
o_hazard_unit_flush_mem | 1 | 
o_hazard_unit_flush_wb | 1 | 

## Slide 63: Base-I | RV64I Design: Hazard Unit
For RV64I Base:
  RAW data hazards occur when an instruction depends on a result that has not yet been written.
  RAW can be resolved by forwarding if the result is computed soon enough.
    Otherwise, stalling the pipeline until the result is available.

## Slide 64: Base-I | RV64I Design: Hazard Unit
RAW Hazard Example:

## Slide 65: Base-I | RV64I Design: Hazard Unit
SW Solution to RAW Hazard Example:

## Slide 66: Base-I | RV64I Design: Hazard Unit
HW Solution to RAW Hazard Example: "Forwarding"

## Slide 67: Base-I | RV64I Design: Hazard Unit
Forwarding is necessary when an instruction in the Execute stage has a source register matching the destination register of an instruction in the Memory or Writeback stage.

## Slide 68: Base-I | RV64I Design: Hazard Unit
Unfortunately, the lw instruction does not finish reading data until the end of the Memory stage, so its result cannot be forwarded to the Execute stage of the next instruction.
We say that the lw instruction has a two-cycle latency.

## Slide 69: Base-I | RV64I Design: Hazard Unit
Solution to lw hazard: "Stall"

## Slide 70: Base-I | RV64I Design: Hazard Unit
Note that the Execute stage is unused in cycle 4.
The bubble is introduced by zeroing out the Execute stage control signals during a Decode stage stall.
  so that the bubble performs no action and changes no architectural state.

## Slide 71: Base-I | RV64I Design: Hazard Unit
For RV64I Base:
  Control hazards occur when the decision of branching has not been made by the time the next instruction must be fetched.
  Control hazards can be resolved by stalling the pipeline until the decision is made or by branch prediction.
  Moving the decision as early as possible minimizes the number of instructions that are flushed on a misprediction.

## Slide 72: Base-I | RV64I Design: Hazard Unit
The beq instruction presents a control hazard: "Flush"

## Slide 73: Base-I | RV64I Design: Hazard Unit
The processor predicts that branches are not taken and simply continues executing the program in order until PCSrcE is computed.

## Slide 74: Base-I | RV64I Design: Hazard Unit
For RV64M:
  Data Hazard occur when an instruction depends on the Multiplication/Division result.
  This Data Hazard is resolved by stalling the pipeline depending on two flags from the M-extension:
    m_done
    m_busy

## Slide 75: Base-I | RV64I Design: Hazard Unit
For Caches:
  The Cache hazards occur when a cache miss happens.
  The Cache hazards can be resolved by stalling the pipeline until fetching new data from the memory.

## Slide 76: Base-I | RV64I Design: Hazard Unit
For CSR:
  The CSR hazards occur when there is an interrupt, or an exception.
  The CSR hazards can be resolved by flushing all the pipes starting from the ID pipe.

## Slide 77: Chapter 3 Implementation of Compressed ISA

## Slide 78: C-Extension : Compressed Decoder
Block Diagram
I/O | Width | Description
i_compressed_decoder_instr | 32 | Input Compressed/Normal Instruction.
o_compressed_decoder_instr | 32 | Output Compressed/Normal Instruction.
o_compressed_decoder_is_compressed | 1 | Output Flag indicates that the input instruction is compressed.
o_compressed_decoder_illegal_instr | 1 | Output Flag indicates that the input instruction is illegal.

## Slide 79: C-Extension : Compressed Decoder
This chapter describes the RVC-Extension which reduces the size of common integer instructions to 16 bits.
  By reducing the sizes of the control, immediate, and register fields.
  The subset was selected to cover the most used instructions in their most used form.
C extension decreases cost, power, and required memory.

## Slide 80: C-Extension : Compressed Decoder
According to the RISC-V Instruction Set Manual, typically 50% to 60% of a program’s instructions can be replaced with RVC instructions, resulting in a 25%–30% code-size reduction.
The C extension allows 16-bit instructions to be freely intermixed with 32-bit instructions.
  The decoder checks on the two LSBs, "11" is the normal 32-bit instruction encoding.

## Slide 81: C-Extension : Compressed Decoder
Compressed Instruction Formats:
  CR, CI, and CSS can use any of the 32 RVI registers.
  CIW, CL, CS, CA, and CB are limited to just 8 of them.

## Slide 82: C-Extension : Compressed Decoder
Registers specified by the three-bit rs1 ′, rs2 ′, and rd ′ fields of the CIW, CL, CS, CA, and CB formats:
  these popular registers, which correspond to registers x8 to x15.

## Slide 83: C-Extension : Compressed Decoder
The formats were designed to:
  keep bits for the two source registers in the same place in all instructions.
  When the full 5-bit destination register specifier is present, it is in the same place as in the 32-bit RISC-V encoding.
    Otherwise, the destination register field can move.
  Immediate fields have been scrambled, as in the base specification, to reduce the number of immediate muxes required.
RVC Instruction Set is divided to 4-quadrants of the encoding space.
  The last quadrant "11" is the normal 32-bit instruction.

## Slide 84: C-Extension : Compressed Decoder
Several instructions are only valid for certain operands; when invalid, they are marked either:
  RES to indicate that the opcode is reserved for future standard extensions.
  NSE to indicate that the opcode is reserved for custom extensions.
  HINT to indicate that the opcode is reserved for microarchitectural hints.
    HINTs instructions do not modify any architectural state and are executed as no-ops on implementations that ignore them.
    Example:
      rd=x0 (e.g. C.ADD x0, t0).
      rd is overwritten with a copy of itself (e.g. C.ADDI t0, 0).

## Slide 85: C-Extension : Compressed Decoder
RVC Instruction Set Listings for Quadrant-0

## Slide 86: C-Extension : Compressed Decoder
RVC Instruction Set Listings for Quadrant-1

## Slide 87: C-Extension : Compressed Decoder
RVC Instruction Set Listings for Quadrant-2

## Slide 88: C-Extension : Compressed Decoder
RVC Expansion to RVI:Sheet Link

## Slide 89: Chapter 4 Implementation of M ISA

## Slide 90: Integer Multiplication And Division Instructions Extension
Instruction | Format | Opcode | Funct3 | Funct7 | Description
mul | R | 0110011 | 0x0 | 0x01 | rd = (rs1 * rs2)[63:0]
mulh | R | 0110011 | 0x1 | 0x01 | rd = (rs1 * rs2)[127:64]
mulhsu | R | 0110011 | 0x2 | 0x01 | rd = (rs1 * rs2)[127:64]
mulhu | R | 0110011 | 0x3 | 0x01 | rd = (rs1 * rs2)[127:64]
div | R | 0110011 | 0x4 | 0x01 | rd = rs1 / rs2
divu | R | 0110011 | 0x5 | 0x01 | rd = rs1 / rs2
RV64M ISA introduces a total of thirteen multiplication and division instructions as shown in the table.

## Slide 91: Integer Multiplication And Division Instructions Extension
Instruction | Fromat | Opcade | Funct3 | Funct7 | Description
rem | R | 0110011 | 0x6 | 0x01 | rd = rs1 % rs2
remu | R | 0110011 | 0x7 | 0x01 | rd = rs1 % rs2
mulw | R | 0111011 | 0x0 | 0x01 | rd = rs1[31:0] * rs2[31:0] (sign extend)
divw | R | 0111011 | 0x4 | 0x01 | rd = rs1[31:0] / rs2[31:0] (sign extend)
divuw | R | 0111011 | 0x5 | 0x01 | rd = rs1[31:0] / rs2[31:0] (sign extend)
remw | R | 0111011 | 0x6 | 0x01 | rd = rs1[31:0] % rs2[31:0] (sign extend)
remuw | R | 0111011 | 0x7 | 0x01 | rd = rs1[31:0] % rs2[31:0] (sign extend)

## Slide 92: Control Signals of M-Extension
Control Signal from main decoder:
  IM_Sel: it acts as an enable signal for the M-extension block and as a select signal for a 2x1 multiplexer. This mux chooses between the output of the M-extension block and the ALU block.
  IsWord: specifies the word instructions
Control Signal from ALU decoder:
  ALUControl: 4-bit signal to specify one instruction from M-extension instruction

## Slide 93: Microarchitecture of M-Extension.

## Slide 94: Microarchitecture of M-Extension.
The microarchitecture consists of:
  Input Blocks
  Multiplication and Division Blocks
    Performing unsigned operations
  Output blocks
  Controller

## Slide 95: Multiplier
Mul_in Block:
  adjust the two inputs srcA and srcB to get the proper multiplicand and multiplier

## Slide 96: Multiplier
Each instruction needs a proper adjustment.
  mul and mulh: if either one of the two inputs is negative, get its positive value using two’s complement.
  mulhsu: if the multiplicand is negative, get its positive value using two’s complement.
  mulhu: no adjustment needed.
  mulw: take only the first 32-bit since it’s a word operation and get the positive value if there is a negative input.

## Slide 97: Multiplier
Booth Block:
  Performs the multiplication using fast algorithm

## Slide 98: Multiplier
Multiplier Algorithm:
  Initialization
    Load the multiplier.
    Set the counter to 64 (for 64-bit multiplication).
  Iterative Multiplication in MUL State:
    Check the LSB of the multiplier.
    If 1, add the multiplicand to the accumulator, if 0, do nothing
    Perform an arithmetic right shift on the combined registers {carry, accumulator, and multiplier}.
    Decrement counter.
  Result
    If the counter reaches 0, the result is in the combined accumulator and multiplier.

## Slide 99: Multiplier
Mul_out Block:
  responsible for adjusting the sign of the product result of the signed instructions (Mul, Mulh, Mulhsu and Mulw).

## Slide 100: Divider
Div_in Block:
  Same as the multiplier we need to adjust the inputs of the operation, Since the non-restoring algorithm is unsigned

## Slide 101: Divider
Non_restoring block:
  responsible for performing the division.

## Slide 102: Divider
Non-Restoring Algorithm:

## Slide 103: Divider
Non-Restoring Algorithm:

## Slide 104: Divider
Non-Restoring Division Steps:
  In this step, the corresponding values are initialized in the registers as follows: register A is set to 0, register M holds the Divisor, register Q contains the Dividend, and N specifies the number of bits in the Dividend.
  In this step, we will check the sign bit of A.
  If the bit in register A is 1, shift the combined value of AQ to the left and perform the operation A = A + M. If the bit is 0, shift the combined value of AQ to the left and perform the operation A = A - M. In the case of 0, this involves adding the 2's complement of M to register A, with the result stored in A.

## Slide 105: Divider
Non-Restoring Division Steps:
  check the sign bit of A again.
  If the bit in register A is 1, then Q[0] will be set to 0. If the bit is 0, then Q[0] will be set to 1. Here, Q[0] refers to the least significant bit of Q.
  Then, the value of N, which serves as a counter, will be decremented.
  If the value of N = 0, then we will go to the next step. Otherwise, we must again go to step 2.
  If the sign bit of register A is 1, we will execute A = A + M.
  In this step, register A holds the remainder, and register Q contains the quotient.

## Slide 106: Divider
Div_out Block:
  responsible for adjusting the sign of the product result of the signed instructions (div, divw, rem and remw).
  Assign the quotient or the remainder to the output of the block according to the instruction (division or remainder)

## Slide 107: M-Extension Controller
Its primary role is to ensure efficient and accurate execution of M-Extension instructions by coordinating the necessary control signals and handling data flow within the processor.
The controller optimizes performance by implementing fast paths for simple operations (fast operations).

## Slide 108: M-Extension Controller
The finite state machine of the controller block which have four states:
  IDLE
  MUL: Performs multiplication
  DIV: Performs division
  FAST: Performs fast operations

## Slide 109: M-Extension Controller

## Slide 110: M-Extension Controller
Block Diagram:

## Slide 111: M-Extension Controller
Fast Operations:
  We added Another feature to the implementation of the M-Extension, which is fast operations, fast operations mean preforming the basic operations during only one clock cycle and not waiting 64 clock cycles.
  We created two registers, one for double word instructions and the other for word instructions. Each one is 7-bit wide. These two registers indicate whether one of the operands is -1, 0, 1, or indicate an overflow value.
Fast DW Reg | B = -1 | B = 1 | B = 0 | A = -1 | A = 1 | A = 0 | Overflow
Fast W Reg | B = -1 | B = 1 | B = 0 | A = -1 | A = 1 | A = 0 | Overflow

## Slide 112: M-Extension Controller
Assuming A is the dividend or multiplicand, and B is divisor or multiplier, then, Fast operations are as shown in the below table
Fast_reg | Instr | Operation | Fast_out
7’b1000001 | REM | Overflow | 0
 | DIV |  | 64’h8000_0000_0000_0000
7'b001xxx0 | REM(U) | A%0 | A
 | DIV(U) | A/0 | 64’hFFFF_FFFF_FFFF_FFFF

## Slide 113: M-Extension Controller
Fast Reg | Instruction | Operation | Fast_Out
7'b1000000 | REM(U) | A%-1 | 0
 | DIV(U) | A/-1 | 2’s comp of A
 | MUL | A*-1 | 2’s comp of A
 | MULH(SU)(U) |  | 64’hFFFF_FFFF_FFFF_FFFF
7’b0100000 | REM(U) | A%1 | 0
 | DIV(U) | A/1 | A
 | MUL | A*1 | A
 | MULH(SU)(U) |  | not fast operation
7'b1001000 | REM(U) | -1%-1 | 0
 | DIV(U) | -1/-1 | 1
 | MUL | -1*-1 | 1
 | MULH |  | 0
 | MULHSU(U) |  | not fast operation

## Slide 114: M-Extension Controller
Fast Reg | Instruction | Operation | Fast_out
7'b1000100 | REM(U) | 1%-1 | 0
 | DIV(U) | 1/-1 | -1
 | MUL | 1*-1 | -1
 | MULH |  | -1
 | MULHSU(U) |  | not fast operation
7'b0101000 | REM(U) | -1%1 | 0
 | DIV(U) | -1/1 | not fast operation
 | MUL | -1*1 | -1
 | MULH |  | 0
 | MULHSU(U) |  | -1
7'b0000100 | REM(U) | 1%B | 1
 | DIV(U) | 1/B | 0
 | MUL | 1*B | B
 | MULH(SU)(U) |  | 0

## Slide 115: M-Extension Controller
Output flag signals:
  Done: Indicates that an operation has completed.
  Div_by_zero: Indicates a division by zero has occurred.
  Overflow: Indicates that an overflow has occurred.
  Busy: Indicates that M unit is currently busy.

## Slide 116: Chapter 5 Caches and Atomic ISA

## Slide 117: Memory Hierarchy
These memory hierarchy components are attached to the processor in a
hierarchical fashion to provide an overall storage system that
approximates the five idealisms infinite capacity, infinite bandwidth, zero latency, persistence, and zero cost as closely as possible.

## Slide 118: Locality principles:
The memory-access patterns of programs are not random.
Accesses tend to repeat themselves in time and/or be near each other in the memory address space.
we have observed that a program’s memory references tend to be localized in time and space.

## Slide 119: Locality principles:
Temporal Locality
the tendency of programs to use data items over and again during their execution
Spatial Locality
Spatial locality arises because of the tendency of programmers and compilers to cluster related objects together in the memory space.

## Slide 120: Caches Organization and Design:
Q1: Where can a block be placed in the upper level? (block placement)
Q2: How is a block found if it is in the upper level? (block identification)
Q3: Which block should be replaced on a miss? (block replacement)
Q4: What happens on a write? (write strategy)

## Slide 121: Block Placement
We have several types of block placement
Direct Mapping : If each block has only one place it can appear in the cache, the cache is said to be direct mapped.

## Slide 122: Block Placement
Fully Associative : Each block in the memory can be mapped to any block on the cache.

## Slide 123: Block Placement
N way set associative: Caches are divided into sets and each set has N number of blocks where a block in the main memory is mapped to a certain set and placed anywhere in the set.

## Slide 124: Where can a block be placed in the upper level?
For our core, we will choose Direct Mapping for the Caches, so it is easy to implement and not complicate the design as we have only a single core.

## Slide 125: Block Identification
The address as we know in direct mapping is mapped to a certain location in the cache, so it is considered a many-to-one mapping.
So, to access a desired location to see if it is a miss or a hit, we will divide the address to : Index and Tag.
It is worth to notice that only one comparison operation is done

## Slide 126: Block Replacement
When a miss occurs, then we should get the desired block from the memory and so we need to put in replacement of another block.
In our desire in direct mapping cache , we won’t need any algorithm since for a block to be placed it has only one place to be placed in (many-to-one mapping) so it is placed in that location anyway.
In simple words: Only one block frame is checked for a hit, and only that block can be replaced if it is a miss.

## Slide 127: Write Strategy
The write policies often distinguish cache designs. There are two basic options when writing to the cache:
Write-through :The information is written to both the block in the cache and to the block in the lower-level memory.
Write-back : The information is written only to the block in the cache. The modified cache block is written to main memory only when it is replaced.
We will choose the Write-through as it has the advantage that the next lower level has the most current copy of the data, which simplifies data coherency which is important for I/O.

## Slide 128: Write Strategy
What happens if the cache doesn’t have the location to be written to ? (write miss).
We have to policies :
Write allocate : The block is allocated on a write miss, followed by the write hit actions above. In this natural option, write misses act like read misses.
No-write allocate : This apparently unusual alternative is write misses do not affect the cache. Instead, the block is modified only in the lower-level memory.
We will choose the Write allocate in our cache as it is most probably a store instruction is followed by a load for that same address place again.

## Slide 129: Conclusion

## Slide 130: Instruction Cache
Its Implementation is the same as Data Cache but with no writing mechanism and it is always reading from the address provided as long as it is a cache hit.

## Slide 131: Microarchitecture

## Slide 132: Cache States

## Slide 133: Added Signals
Since we have Compressed instructions, we jump 2 locations when we encounter such an instruction.
This may cause an instruction to be present in TWO
different cache lines.
That can happen when 2 bytes are in the last 2 bytes of a line and the other 2 bytes are at the beginning of the next cache line.
To solve this problem, we added the OFFSET signal

## Slide 134
Address 1
Address 2
OFFSET signal

## Slide 135: DATA CACHE
Unlike the instruction cache, the data cache has more control signals and have writing mechanism.
We started by implementing the data cache without Atomic instructions, then we extended our implementation to the A extension.

## Slide 136: Cache Address Specs
[63:12] | [11:5] | [4:3] | [2:0]
TAG | INDEX | BLOCK_OFFSET | BYTE_OFFSET
BYTE_OFFSET : Since each Doubleword (DW) is 8 bytes so we need these 3-bits for the byte offset in each DW.
BLOCK_OFFSET: Since we have 4 DW in each block so we need 2-bits to identify the needed DW.
INDEX: Since we have 4KiB and each block has 4 DW and each DW has 8 bytes then we have 128 so we need for the INDEX 7-bits to identify the needed block.
TAG : Each block has its own TAG bits which are the rest of the 64-bit address to uniquely identify the block and check if it is a miss or hit.

## Slide 137: Data Cache Block Diagram

## Slide 138: Data Cache Controller States
IDLE
MEM_REQ
UPDATE_CACHE
MEM_WRITE
Load && cache_hit
cache_miss
update is done
store instruction
write is done

## Slide 139: Some Cache Cases: Read Hit

## Slide 140: Read Miss

## Slide 141: Write Hit

## Slide 142: Atomic Extension “A”
lr.w | sc.w | amoswap.w | amoadd.w | amoand.w | amoor.w | amoxor.w | amomax.w | amomin.w | amomaxu.w | amominu.w
lr.d | sc.d | amoswap.d | amoadd.d | amoand.d | amoor.d | amoxor.d | amomax.d | amomin.d | amomaxu.d | amominu.d
The standard atomic-instruction extension, named “A”, contains instructions that atomically
read-modify-write memory to support synchronization between multiple RISC-V harts running
in the same memory space.
The two forms of atomic instruction provided are load-reserved/store-conditional
instructions and atomic fetch-and-op memory instructions.

## Slide 143: Atomic Extension “A”
LR/SC : “LR” is x[rd] = MEM[x[rs1]] AND then locks MEM[x[rs1]]
“SC” puts on x[rd] zero if store is succussed and non-zero if failure
For AMO: it can be divided in 3 separate instructions as follows:
Load
Operation
Store
x[rd] = MEM[x[rs1]] , MEM[x[rs1]] = MEM[x[rs1]] OPERATION x[rs2]
Load
Operation
Store

## Slide 144: Modified Data Cache For “A” Extension

## Slide 145: Modified Data Cache Controller States
IDLE
MEM_REQ
AMO_OP
UPDATE_CACHE
MEM_WRITE
Load && cache_hit
cache_miss
update is done
store instruction
amo instruction
write is done

## Slide 146: Note on MEM_WRITE State in atomic
Since we have the write happens with positive edge with clock, when we have AMO, we write in the main memory first before the cache unlike the ordinary store.
That’s because we don’t want to override the old data before it reaches the rd.
So, when the “write_done” comes, we rise “i_write” from controller to memory and release “stall” so that next positive edge, old data passes to WB Stage and AMO result is written inside cache.

## Slide 147: Caches and Main Memory
Since we have 2 read ports (for the case of cache miss) one for each cache, and 1 write port for data cache, we need to determine how the interface with our main memory will be.
After reviewing "Modular Multi-Ported SRAM-based Memories," in Proceedings of the 2014 ACM/SIGDA International Symposium on Field-programmable Gate Arrays (FPGA '2014), February 2014 by Ameer M.S. Abdelhadi and Guy G.F. Lemieux, We decided to use the memory arbiter approach to serve both caches.

## Slide 148: Memory Arbiter
We implemented the main memory on the Block Ram (BRAM) of our FPGA.
We partitioned the Main Memory into instruction part and data part.
The instruction memory starts at address 0x000000000, and the data memory starts at address 0x001000000.
The Memory Arbiter serves both the instruction and data caches at cache misses and when data cache wants to write on main memory.

## Slide 149: Block Diagram for Memory Arbiter
MEM_ARBITER
bit
64-
block_address
bit
256-
block_data
mem_read_req
mem_read_done
i_cache_interface
64-
bit
block_address
256-
bit
block_data
mem_read_req
mem_read_done
d_cache_interface
64-
bit
mem_write_data
mem_write_req
mem_write_strobe
8-
bit
64-
bit
mem_write_address
mem_write_done
MAIN_MEM
256-
bit
block_data
mem_read_req
mem_read_done
64-
bit
mem_write_data
mem_write_req
mem_write_strobe
8-
bit
64-
bit
mem_write_address
mem_write_done
64-
bit

## Slide 150: Branch Prediction in RISC-V
Branch Penalties limit the performance of the core and increases CPI beyond 1.
Branch prediction with high accuracy can reduce branch penalties.

## Slide 151: What is Control Transfer?
Control Transfer instructions causes the program flow to change to another address in the instruction memory.
This means we have two things to determine to execute these instructions:
Decision ( Taken or Not Taken)
Target Address

## Slide 152: Static Prediction
First type of prediction is static prediction by always take the same decision for all control flow instructions.
Overall probability a branch is taken is ~60-70% with the following distribution according to the direction of branch.

## Slide 153: Static Predictor
By this previous knowledge, the design of static predictor block can be as follows:
Take the Jump when the instruction is decoded as Unconditional Jump.
Prefer the backward branch, by taking the branch if the offset is negative.
We will put predictor in the ID Stage.

## Slide 154: Static Prediction Accuracy
The accuracy of Static Predictor ranges from 50 to 80 % , in addition to at least 1 bubble is introduced either the prediction is right or wrong.
Therefore, we need another type for better accuracy and performance

## Slide 155: Dynamic Prediction
Dynamic Prediction makes use of the actual branch decisions to update itself and dynamically perform better.
How is that achieved?

## Slide 156: Introducing Branch History Table (BHT)
It is a table that contains all previous control transfer instructions according to their corresponding PC.
For each prediction , BHT updates its next decision by comparing its prediction with the actual right decision produced from the Branch Unit.
It uses a Two-Bit Counter to update its decision every time the same branch instruction is encountered.

## Slide 157: Two Bit Counter
It is an FSM that updates the decision of each branch instruction according to past behavior.
If the current state is strong taken or weak taken, then the decision is to take the branch. Otherwise , it is not taken.
According to the output of the branch unit in the EX-stage to that branch instruction, the state is updated.

## Slide 158: How BHT works
Valid | Two Bit Saturation
0 | 00
0 | 00
0 | 00
0 | 00
Assume a Loop with 10 iterations, first time is mis predicted.

## Slide 159: After 1st Branch encounter with TAKEN decision
Valid | Two Bit Saturation
1 | 01
0 | 00
0 | 00
0 | 00
Also , Second time is mis predicted.

## Slide 160: After 2nd Branch encounter with TAKEN decision
Valid | Two Bit Saturation
1 | 10
0 | 00
0 | 00
0 | 00
Next Prediction will be “Taken” for the rest of the Loop Iterations.

## Slide 161: After 3rd Branch encounter with TAKEN decision
Valid | Two Bit Saturation
1 | 11
0 | 00
0 | 00
0 | 00
Strongly Taken

## Slide 162: After first NOT TAKEN decision at the end of the Loop
Valid | Two Bit Saturation
1 | 10
0 | 00
0 | 00
0 | 00
If the Loop is initialized again , it will be predicted right from the first time!
Weak Taken

## Slide 163: Decision Prediction is Done!
Now we solved half of the problem but, we want to know where to go if the branch is taken ?

## Slide 164: Introducing: Branch Target Buffer (BTB)
From the past behavior of the branch instruction , we can also determine the Target address to branch to.
Also, for JALR instruction the Target address can be changed every few times the instruction is encountered.
BTB saves the Target Address of the branch instructions according to the PC of it.

## Slide 165: How BTB works
Valid | Target address
0 | 32’h0000_0000
0 | 32’h0000_0000
0 | 32’h0000_0000
0 | 32’h0000_0000

## Slide 166: After 1st Branch encounter
Valid | Target address
1 | 32’h0008_0F00
0 | 32’h0000_0000
0 | 32’h0000_0000
0 | 32’h0000_0000

## Slide 167: Added Modules for Dynamic Branch Prediction
We added the following Modules :
Branch Predictor : in the IF stage.
Branch Recovery : in the EX stage
Next PC Logic : in the IF stage

## Slide 168: Branch Predictor

## Slide 169: Branch Prediction Address Specs
[63:10] | [9:1]
TAG | INDEX
INDEX: We have 512 so we need for the INDEX 9-bits to identify the needed block starting from bit “1” as bit “0” is always zero.
TAG : Each block has its own TAG bits which are the rest of the 64-bit address to uniquely identify the block and check if it is a miss or hit.

## Slide 170: Branch Prediction Entry Contents
Valid | TAG | Saturation Bits | Target Address
1-bit | 54-bits | 2-bits | 64-bits
Valid: To indicate that the entry has a valid branch instruction contents.
TAG: To check that current PC is same as entry contents.
Saturation Bits: Two-bit saturation to save branch history decision.
Target Address: To indicate the Target address in case of prediction Taken.

## Slide 171: Branch Recovery
flush

## Slide 172: Next PC Logic

## Slide 173: Dynamic Prediction Accuracy
By using BHT and BTB , prediction accuracy can range from 80 to 95% which will increase our performance ,decrease bubbles and help in limiting the CPI to 1.

## Slide 174: Chapter 6 Privileged architecture

## Slide 175: Importance of privileged ISA
In order to run an operating system on our microprocessor, we need to implement the privileged architecture, which provides three main capabilities:
Security and isolation
Context switching
Trap handling

## Slide 176: Privileged software stack
RISC-V can support multiple of software stacks, but since we are targeting to run a LINUX-OS, we chose the implementation stack shown in figure.
It provides clean split between
Layers of the software stack

## Slide 177: Privileged software stack
This configuration shows that a conventional operating system can support multiprogrammed execution of multiple application.

## Slide 178: Privilege levels
At any time, the core is running at some privilege level encoded as a mode in one or more CSRs (control and status registers).
Three RISC-V privilege levels are currently defined as shown in table
Level | Encoding | Name | Abbreviation
0 | 00 | User/application | U
1 | 01 | Supervisor | S
2 | 10 | Reserved | 
3 | 11 | Machine | M

## Slide 179: CSRs
Each privileged mode adds a few operations, and Control/Status Registers (CSRs) that control operations.
CSRs are mode-sensitive, accessible only by code running at a specific privilege mode or higher.
There are (often) multiple CSR copies/views for each mode.
Control/Status Regs (CSRs) have their own address space.

## Slide 180: CSR address space
The standard RISC-V ISA sets aside a 12-bit encoding space (csr[11:0]) for up to 4,096 CSRs. By convention, the upper 4 bits of the CSR address (csr[11:8]) are used to encode the read and write accessibility of the CSRs.
The top two bits (csr[11:10]) indicate whether the register is read/write (00, 01, or 10) or read-only (11). The next two bits (csr[9:8]) encode the lowest privilege level that can access the CSR.

## Slide 181: Machine-level ISA
The machine level has the highest privileges and is the only mandatory privilege level for a RISC-V hardware platform.
Machine mode has access to all the underlying hardware.
Machine-Level CSRs provide essential information and functionalities to the core.

## Slide 182: Machine-level ISA
Here's a subset of the implemented machine-mode CSRs:
Trap setup | Mstatus, medeleg, mideleg, mtvec, mie
Trap handling | Mepc, mip, mcause, mtval, mscratch

## Slide 183: Supervisor-level ISA
Supervisor level is two layers below the machine-level, it has access to CSRs of supervisor mode and user mode.
RISC-V provides a security mechanism that restricts user applications from accessing critical system resources directly.
Supervisor mode is responsible for handling interrupts and exceptions.

## Slide 184: Supervisor-level ISA
Here's a subset of the implemented supervisor-mode CSRs
Trap setup | Sstatus, stvec, sie
Trap handling | Sepc, sip, scause, stval, sscratch

## Slide 185: CSR instructions

## Slide 186: Exceptions and interrupts
Exceptions: synchronous events
Synchronous: caused by a specific instruction execution.
Interrupts: Asynchronous events. Not caused by an instruction : I/O, timer, SW (from another hart)
Both handled identically by trapping

## Slide 187: Interrupts and exceptions
The core supports external and timer interrupts.
In our implementation, there’s no machine-level interprocessor interrupts as we have one hart so there’s no software interrupts.
External interrupts take priority over timer interrupts.
Machine-level interrupts take priority over supervisor-level interrupts.

## Slide 188: Interrupts and exceptions
The core supports a set of exceptions as shown in table
Interrupts take priority over exceptions
Priority | Code | Description
Highest | 2 | Illegal instruction
 | 0 | Instruction address misaligned
 | 11 | Environment CALL
 | 3 | Environment BREAK
 | 7 | Store access fault
Lowest | 5 | Load access fault

## Slide 189: Interrupts and exceptions
Where to trap:
XTVEC: holds the handler address
XI/EDELEG: select mode to trap into
Reason for trap:
XCAUSE: holds the trap ID
XTVAL: holds additional information about the cause
How to return from trap:
XEPC: saves the return program counter
XSTATUS: saves the current mode

## Slide 190: Trap setup
Interrupt/Exception delegation:
Traps always sent to m-mode by default
It can be sent to lower privilege mode to reduce the overhead, but not to less privileged to the one that trapped.
Interrupts are delegated only if the corresponding enable bit is set

## Slide 191: Trap setup and handling
The ASM chart shown realizes the task of handling traps

## Slide 192: Trap setup
Ideally the core is in the idle state, when a trap occurs:
1-Flush the pipeline
2-Check the current operating mode
A-If it’s m-mode:
1) Set mstatus_mpp to 2’11
2) Set the values of mepc, mtval, mtinst, and mcause CSRs
3) Move to setting_up state
B-If it’s s-mode and the trap is delegated:
1) Set mstatus_spp and sstatus_spp to 1’b1
2) Set the values of sepc, stval and scause CSRs
3) Move to setting_up state

## Slide 193: Trap setup
C-If it’s s-mode and the trap is not delegated:
1) Set mstatus_mpp to 2’b01
2) Set the values of mepc, mtval, mtinst, and mcause CSRs
3) Move to setting_up state.
3- Disable interrupts globally
4- Set PC to the address of the handler
5- Return to the idle state

## Slide 194: Trap return
To return after handling a trap, there are separate trap return instructions per privilege level, MRET and SRET.
Once xret instruction is met at the end of the trap handler the following steps happen:
1- Flush the pipeline
2- Return to the previous privilege mode
3- xRET sets the pc to the value stored in the xepc register.
4- Set xie to the value stored in xpie, set xpie to 1

## Slide 195: RV64IMAC Architecture with privilege modes

## Slide 196: Chapter 7 Verification

## Slide 197: Verification Process
Verification Plan
Direct testbench
Random Testbench

## Slide 198: Verification Plan
Verification plan shows the scenarios to be tested for each instruction and to test specific scenarios like forwarding and hazard insertion, for a high function coverage.

## Slide 199: Direct testbench
Direct testbench was used to check the connections between modules for easy debugging and to check the basic functionality of the design modules.

## Slide 200: Direct testbench
Direct testbench methodology:
      Create the scenario to be tested.
      Create the sequence of instructions that test this scenario.
      Compile assembly to binary.
      Use ISS simulator as a golden reference mode.

## Slide 201: Direct testbench
Direct testbench assumptions:
      All Registers are initialized by the equation RF[i] = 2 x i
      All Data Memory locations are initialized by the equation Mem[i]= I
      Ripes simulator has considered as a golden reference for us.
      We have set the sources and destination to be the same for all to check one location only (we didn’t consider forwarding at this stage).

## Slide 202: R-Type

## Slide 203: R-Type
Link

## Slide 204: R - TYPE
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
OUR OUTPUT

## Slide 205: I - TYPE

## Slide 206: I - TYPE

## Slide 207: I - TYPE
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
OUR OUTPUT

## Slide 208: Load instructions

## Slide 209: S-type

## Slide 210: U-type

## Slide 211: STORE/LOAD/ U-TYPE

## Slide 212: STORE/LOAD/U-TYPE
.
.
.
.
.
.
.
.
.
.
.
1. .
2. .
.
.
.
.
.
.
.
.
.
.
.
1. .
2. .
OUR OUTPUT

## Slide 213: BRANCH/JUMP

## Slide 214: JUMP
16 + 0B = 21
1. . jal x17 56
4 + 38 = 3c
2. . jalr x17 x11 11
OUR OUTPUT
1. .
2. .

## Slide 215: Random Testbench Verification
Random Testbench Verification steps:
      Setting up the Environment.
      Use random instruction generator.
      Use ISS simulator as a golden reference mode..

## Slide 216: Setting up the Environment.
Linux environment.
UVM simulator.
RISC-V simulator ISS.
RISC-V toolchain.
elf to hex tool.

## Slide 217: Testing Environment and Instruction Generator
Riscv-dv by google and chipallinece.
Riscv-tests by imperas and microchip.

## Slide 218: Comparison between ISS simulators

## Slide 219: RISC-V DV
It is a testing environment that can generate high-coverage tests for each extension. Figure 63 shows the flow of RISC-V DV.

## Slide 220: RISC-V DV
The output files

## Slide 221: Random Testbench Verification
Testing Steps for Each Extension:
      Edit the test parameters in Yamal file to choose the extension , instructions and scenarios you want to cover it.
      Generating the random test code assembly from riscv-dv environment.
      Compiling the assembly file with linker script using the RISC-V toolchain.
      Running ISS with the elf file and the log that is the change in registers after each instruction.
      Converting elf file to hex file using elf-to-hex tool.
      Load our instruction memory with the hex file and start the simulation.
      Debug and trace if there’s a mismatch.
      Report the scenario that make that error to design team.
We followed these steps for each extension even with privileged extensions but in atomic extension, the riscv-dv doesn’t support it so we go with direct tests again.

## Slide 222: Testing the Core with Caches
Testing the core after adding caches: Regression tests have been done with random tests for store and load and direct tests that test cache-miss scenarios.
Run a program: An assembly-written program compiled and converted to hex to send data on the UART bus to test the capability of the system to run full programs.

## Slide 223: Compilation Process
The Compiler
ABI Library

## Slide 224: Compilation Process
The compiling command
The disassemble command
The elf-to-hex command
Then you can load the Hex to your design and the Elf file to ISS then compare the results and debug.

## Slide 225: Chapter 8 FPGA Implementation

## Slide 226: FPGA implementation and applications
I. Implementation:
Constrains
Synthesis Reports
Implementation Reports
II. Applications:
LEDs Testing
Sending Characters using UART

## Slide 227: FPGA implementation and applications
I. Implementation:
Constrains
Synthesis Reports
Implementation Reports
II. Applications:
LEDs Testing
Sending Characters using UART

## Slide 228: Constrains
Constrains file role
It helps mapping the Ball-Grid-Array (BGA) pins on the actual Xilinx FPGA for more human-readable names.
It defines critical hardware settings that affect how the FPGA interfaces with other components.
constraints define the operating voltage, clock source and its frequency and the physical pins and connect it to a certain port.

## Slide 229: FPGA implementation and applications
I. Implementation:
Constrains
Synthesis Reports
Implementation Reports
II. Applications:
LEDs Testing
Sending Characters using UART

## Slide 230: Synthesis Reports
Timing Report
Power Report
Utilization Report

## Slide 231: Timing Report
Large setup slack
Negative hold slack

## Slide 232: Synthesis Reports
Timing Report
Power Report
Utilization Report

## Slide 233: Power Report

## Slide 234: Synthesis Reports
Timing Report
Power Report
Utilization Report

## Slide 235: Utilization Report

## Slide 236: Utilization Report

## Slide 237: FPGA implementation and applications
Implementation:
Constrains
Synthesis Reports
Implementation Reports
II. Applications:
LEDs Testing
Sending Characters using UART

## Slide 238: Implementation Reports
Timing Report
Power Report
Utilization Report

## Slide 239: Timing Report

## Slide 240: Implementation Reports
Timing Report
Power Report
Utilization Report

## Slide 241: Power Report

## Slide 242: Implementation Reports
Timing Report
Power Report
Utilization Report

## Slide 243: Utilization Report

## Slide 244: Utilization Report

## Slide 245: FPGA implementation and applications
I. Implementation:
Constrains
Synthesis Reports
Implementation Reports
II. Applications:
LEDs Testing
Sending Characters using UART

## Slide 246: Application 1: LEDs Testing
Objective:
It tests RISC-V specific operations while turning a LED on is the indication to the success of these operations. These operations are as follows:
• Integer (add, or, xor and slt).
• Multiplication.
• Compressed.
• Atomic.

## Slide 247: Application 1: LEDs Testing

## Slide 248: Assembly Program for App 1

## Slide 249: Assembly Program for App 1

## Slide 250: Assembly Program for App 1

## Slide 251: FPGA implementation and applications
I. Implementation:
Constrains
Synthesis Reports
Implementation Reports
II. Applications:
LEDs Testing
Sending Characters using UART

## Slide 252: Application 2: Sending Characters using UART
Objective:
It is to send characters from UART Tx port to PC serial port and read the sent characters by TTY.
System Block Diagram for the App

## Slide 253: Application 2: Sending Characters using UART
System Block Diagram for the App

## Slide 254: Assembly Program for App 2
Note:
if random characters appear on the screen that means there’s a timing mis-synchronization between UART module baud rate and the baud rate on the serial port.

## Slide 255: Chapter 9 ASIC Implementation
Application Specific Integrated Circuit​

## Slide 256: ASIC
ASIC Flow
Synthesis
Formal Verification
DFT
PnR
Signoff/Tape out
The layout is sent to the fab as GDSII or OASIS file format

## Slide 257: Synthesis
What is Logic Synthesis ?
synthesis is the process that translate and map RTL code written in HDL into technology specific gate-level-netlist and optimized for a set of pre-defined constrnais
Synthesis
Design Constrains
Standard cell library
gate-level-netlist
RTL

## Slide 258: Synthesis
Synthesis Flow
Libraries Definitions
Reading Design
Define Design environment Constrains
Compile /Tech-map/opt
Generate Reports
Generate Netlist

## Slide 259: Synthesis
Define Design environment Constrains
1 - Clock Definition
2- set input/output delay on ports
3-Driving cells
4-Output load
5-wireload Model
6-Operating conditions ”PVT”

## Slide 260: Synthesis
Non-linear Delay Models: The delay of cells are stored in non-linear delay models (NLDMs). These models use lookup tables (LUTs) to represent delays as a function of input transition and output load capacitance .

## Slide 261: Synthesis
  View Design Schematic
Start GUI command

## Slide 262: Synthesis
Reports
Setup report : Hold reports : Area report : power report :

## Slide 263: Formal Verification
▶ Logic Equivalence Checking.
▶ Formal Verification is an alternative to verification through
simulation.
▶ As design become larger and more complex and require more
simulation vectors, regression testing with traditional
simulation tools becomes a bottleneck in the design flow.
▶ 100% coverage.
▶ It verifies the logical equivalence of RTL, gate or transistor
level netlist to each other.
▶ Ignores timing information
▶ Only Boolean Equivalence.

## Slide 264: Formal Verification
Formality Flow
▶ There are four basic steps in equivalence checking:
▶load guidance: .svf file
changes name object - optimization register constant - registers merged and Duplicate
▶ Read
▶ Match
▶ Verification
▶ Debug

## Slide 265: DFT
The Design for Test (DFT) stage involves adding hardware components to the ASIC design to facilitate testing. DFT components include test points, scan chains, and boundary scan cells. DFT components are added to the design to enable efficient testing of the ASIC during production.
(DFT) is a design technique used in manufacturing to ensure that a product can be easily and efficiently tested for faults and defects. Here are some common manufacturing faults and defects that DFT aims to identify and mitigate:
1. Open Circuits
Description: Open circuits occur when there is a break in the electrical path, preventing current flow.
2. Short Circuits
Description: Short circuits happen when unintended connections between two points allow current to flow.
3. Solder Bridges
Description: Solder bridges are unintended connections between two conductors caused by excess solder.
DFT Techniques: Automated Optical Inspection (AOI), X-ray inspection.

## Slide 266: DFT
Scan flip-flop & scan chain:
[Scan flipflop design]
[Design with scan chain]
  Shift In (Scan In) — SE = 1
  Capture — SE = 0
  Shift Out (Scan Out) — SE = 1

## Slide 267: DFT
DFT Compiler Flow
  RTL preparation for DFT
Add scan related I/o pins in the design
  SI - SE -So -scan_clk – scan_rst-Test_Mode
[declare the additional inputs and output due to DFT]
[Scan Clk and Scan RST Muxs]

## Slide 268: DFT
DFT FLOW
DFT Constraints
Pre DFT test DRC
DFT insert
Post DFT test DRC
Netlist

## Slide 269: DFT
DRC report and test coverage

## Slide 270: PnR
PNR Processes:
Floor planning
Power planning
Placement
Clock tree synthesis (CTS
Routing
Chip finishing
Floor planning and power planning
Purpose: Define the layout and allocate area for different functional blocks of the ASIC.
Tasks:
  Define core and die area
  Place macros (large blocks such as memory, IP blocks)
  Create power grid and establish power planning
  Define placement of I/O pins
Placement
Purpose: Place standard cells in the defined floorplan.
Tasks:
  Initial placement of standard cells
  Legalization to ensure no cells overlap and are placed in legal positions
Clock Tree Synthesis (CTS)
Purpose: Design the clock distribution network to ensure the clock signal reaches all sequential elements with minimal skew and latency.
Routing
Purpose: Establish electrical connections between placed cells according to the netlist.
Tasks:
  Global Routing: Determine routing paths for each net at a coarse level
  Detailed Routing: Precisely connect all pins and vias according to the global routing plan

## Slide 271: PnR
Place & Routing
Post DFT netlist
.v
Timing (TT,SS,FF) .LIB
RC
Coefficient file .captable
Technology LEF File
.lef
Standard cell LEF
.lef
Timing constains .sdc
Gate Level Netlist .gds

## Slide 272: PnR
Technology LEF (.lef)
Standard cell LEF (.lef)
RC coefficient (.captable)
It contains technology specific characterizations of metal layers vias as well as DRC
It contains abstract view of each standard cell
It contains sheet capacitance and resistance of metal layers

## Slide 273: PnR
Design Import
1- Verilog gate-level-netlist
- Gates from the standard cell library
2-physical/technology library
- technology library LEF
- standard cell library LEF

## Slide 274: PnR
Floor planning
Purpose: Define the layout and allocate area for different functional blocks of
the ASIC.
Tasks:
  Define core and die area
  Place macros (large blocks such as memory, IP blocks)
  Create power grid and establish power planning
  Define placement of I/O pins

## Slide 275: PnR
Power planning :
Power planning is deciding how we will deliver power to the design’s standard cells
Power mech distribution :
Rings : carries VDD and VSS around the chip to connect power to II/o pads
Stripes : carries VDD and VSS from the ring To decrease IR drop
Rails : connect VDD and VSS to standard cells

## Slide 276: PnR
Verify Geometry after power Ring and stripes

## Slide 277: PnR
Placement
Placement is the stage of the design flow, during which each instance (standard cell) is given an exact location.
• Inputs:
• Netlist of gates and wires.
• Floorplan and Technology constraints
• Output:
• All cells located in the floorplan.
• Goal
• Provide legal location of entire netlist
• Avoiding routing congestion, to enable easy detailed routing of all nets
• Meet timing, area, and power targets

## Slide 278: PnR
Placement script

## Slide 279: PnR
Analyze Timing pre cts - setup
3. Clock Tree Synthesis (CTS)
Purpose: Design the clock distribution network to ensure the clock signal reaches all sequential elements with minimal skew and latency.
Clock Tree Synthesis (CTS)
  Tasks:​Insert clock buffers &Balance the clock tree to minimize skew

## Slide 280: PnR
Analyze Timing pre and post cts – Hold
After first trial optimization

## Slide 281: PnR
Routing and chip Finishing :
Purpose: Establish electrical connections between placed cells according to the netlist.
Tasks:
  Global Routing: Determine routing paths for each net at a coarse level
  Detailed Routing: Precisely connect all pins and vias according to the global routing plan
  Resolve DRC (Design Rule Checking) violations and optimize for signal integrity

## Slide 282: PnR
creates physical connections to all clock and signal pins through metal interconnects Routed paths must meet setup and hold timing, max cap/trans, and clock skew requirements Metal traces must meet physical DRC requirements

## Slide 283: PnR
Tape-out
Prepare the final GDSII or OASIS file for manufacturing.
Submit the design to the foundry for fabrication.

## Slide 285
Thank You